## Slide 1: BGP
Border getaway protocol
Dynamic Routing Protocol
Exterior Getaway protocol which communicate with different Autonomous System.
Classification
It comes under Path vector routing
Inter AS routing
We need autonomous system

## Slide 2: Types of Autonomous System
Public Autonomous System (Ranges 1 to 64511)
Private Autonomous System(64511 to 65535)
Types of BGP:
EBGP
IBGP

## Slide 3: IBGP
It is that version of BGP which only Woking under only one AS
Administrative Distance 200
EBGP: which works between different autonomous system
Administrative Distance 20
Neighborship peering (New Feature)
Over Physical IP
Over Loopback IP
Direct Peering
Indirect peering

## Slide 4: More about BGP
Current version BGP 4
Single home environment
Dual home BGP Environment
Single multiple environment
Dual multi home environment

## Slide 5: BGP tables
Neighbour Table
BGP table
IP routing it keeps the record of best path
BGP Packet
Open packet
Keepalive packet
Update Packet
Notification Packet

## Slide 6: BGP Timer
Keepalive timer
Whole timer
States of BGP
Idle state
Connect state
Active state
Open sent
Open confirm
Established

## Slide 7: Distance Vector Routing
The distance vector routing algorithm works by having each router maintain a routing table, giving the best-known distance from source to destination and which route is used to get there. These tables are updated by exchanging the information with the neighbor having a direct link.

## Slide 8
Information kept by DV router -
Each router has an ID
Associated with each link connected to a router,
there is a link cost (static or dynamic).
Intermediate hops
Distance Vector Table Initialization -
Distance to itself = 0
Distance to ALL other routers = infinity number.

## Slide 9: Link State Routing
The Link State Routing Algorithm is an interior protocol used by every router to share the information or knowledge about the rest of the routers on the network. The link state routing algorithm is a distributed algorithm using which every router computes its routing table.

## Slide 10: The three keys to understand the Link State Routing algorithm:
Knowledge about the neighborhood: Instead of sending its routing table, a router sends the information about its neighborhood only. A router broadcast its identities and cost of the directly attached links to other routers.
Flooding: Each router sends the information to every other router on the internetwork except its neighbors. This process is known as Flooding. Every router that receives the packet sends the copies to all its neighbors. Finally, each and every router receives a copy of the same information.
Information sharing: A router sends the information to every other router only when the change occurs in the information.

## Slide 11: Bellman Ford’s algorithm
Dynamic Programming Problems, the algorithm calculates shortest paths in a bottom-up manner. It first calculates the shortest distances which have at-most one edge in the path. Then, it calculates the shortest paths with at-most 2 edges, and so on. After the i-th iteration of outer loop, the shortest paths with at most i edges are calculated. There can be maximum |V| – 1 edge in any simple path, that is why the outer loop runs |v| – 1 time. The idea is, assuming that there is no negative weight cycle if we have calculated shortest paths with at most i edges, then an iteration over all edges guarantees to give the shortest path with at-most (i+1) edges

## Slide 12: Dijkstra’s algorithm
Dijkstra’s algorithm is very similar to Prim’s algorithm for minimum spanning tree. Like Prim’s MST, we generate an SPT (shortest path tree) with a given source as root. We maintain two sets, one set contains vertices included in the shortest-path tree, other set includes vertices not yet included in the shortest-path tree. At every step of the algorithm, we find a vertex which is in the other set (set of not yet included) and has a minimum distance from the source.

## Slide 13: Path Vector Routing
A path-vector routing protocol is a network routing protocol which maintains the path information that gets updated dynamically. Updates that have looped through the network and returned to the same node are easily detected and discarded.

## Slide 14: Open Shortest Path First (OSPF) protocol States
Open Shortest Path First (OSPF) is a link-state routing protocol that is used to find the best path between the source and the destination router using its own Shortest Path First). OSPF is developed by Internet Engineering Task Force (IETF) as one of the Interior Gateway Protocol (IGP), i.e, the protocol which aims at moving the packet within a large autonomous system or routing domain. It is a network layer protocol which works on protocol number 89 and uses AD value 110. OSPF uses multicast address 224.0.0.5 for normal communication and 224.0.0.6 for update to designated router(DR)/Backup Designated Router (BDR).

## Slide 15: OSPF terms –
Router I’d – It is the highest active IP address present on the router. First, the highest loopback address is considered. If no loopback is configured then the highest active IP address on the interface of the router is considered.
Router priority – It is an 8-bit value assigned to a router operating OSPF, used to elect DR and BDR in a broadcast network.

## Slide 16
Designated Router (DR) – It is elected to minimize the number of adjacencies formed. DR distributes the LSAs to all the other routers. DR is elected in a broadcast network to which all the other routers share their DBD. In a broadcast network, the router requests for an update to DR, and DR will respond to that request with an update.