## Slide 1: Network layer
Unicast
Broadcast
Multicast

## Slide 2: Network Address Translation (NAT)
NAT translates the Private IP into Public IP and Public IP into private IP
Network Address Translation (NAT) is a process in which one or more local IP address is translated into one or more Global IP address and vice versa in order to provide Internet access to the local hosts. Also, it does the translation of port numbers i.e. masks the port number of the host with another port number, in the packet that will be routed to the destination.

## Slide 3: NAT inside and outside addresses –
Inside refers to the addresses which must be translated. Outside refers to the addresses which are not in control of an organization. These are the network Addresses in which the translation of the addresses will be done.

## Slide 4: Network Address Translation (NAT) working –
Generally, the border router is configured for NAT i.e the router which has one interface in the local (inside) network and one interface in the global (outside) network. When a packet traverse outside the local (inside) network, then NAT converts that local (private) IP address to a global (public) IP address. When a packet enters the local network, the global (public) IP address is converted to a local (private) IP address.

## Slide 5
Inside local address – An IP address that is assigned to a host on the Inside (local) network. The address is probably not an IP address assigned by the service provider i.e., these are private IP addresses. This is the inside host seen from the inside network.
Inside global address – IP address that represents one or more inside local IP addresses to the outside world. This is the inside host as seen from the outside network.

## Slide 6
Outside local address – This is the actual IP address of the destination host in the local network after translation.
Outside global address – This is the outside host as seen from the outside network. It is the IP address of the outside destination host before translation.

## Slide 7
Static NAT – In this, a single unregistered (Private) IP address is mapped with a legally registered (Public) IP address i.e one-to-one mapping between local and global addresses. This is generally used for Web hosting. These are not used in organizations as there are many devices that will need Internet access and to provide Internet access, a public IP address is needed.

## Slide 8
Dynamic NAT – In this type of NAT, an unregistered IP address is translated into a registered (Public) IP address from a pool of public IP addresses. If the IP address of the pool is not free, then the packet will be dropped as only a fixed number of private IP addresses can be translated to public addresses.

## Slide 9: Public and Private IP Address
A public IP address identifies you to the wider internet so that all the information you're searching for can find you. A private IP address is used within a private network to connect securely to other devices within that same network.
Examples of Private IP Addresses Space:
10.0.0.0 to 10.255.255.255
172.16.0.0 to 172.31.255.255
192.168.0.0 192.168.255.255

## Slide 10
IPv6: This new IP address version is being deployed to fulfil the need for more Internet addresses. It was aimed to resolve issues which are associated with IPv4. With 128-bit address space, it allows 340 undecillion unique address space. IPv6 also called IPng (Internet Protocol next generation).
IPv6 Characteristics:
Realtime Data Transmission
Authentication
Encryption enabled
Fast Processing at routers

## Slide 11: NAT

## Slide 12
Types of IPv6
Unicast addresses It identifies a unique node on a network and usually refers to a single sender or a single receiver.
Multicast addresses It represents a group of IP devices and can only be used as the destination of a datagram.
Anycast addresses It is assigned to a set of interfaces that typically belong to different nodes.